## Slide 1
LECTURE 03b
Fermat's Principle
Optical Path Length · Derivation of All Ray Laws · GRIN Media · Euler–Lagrange · Huygens Connection
Linear Optics Course · All formulas typeset with LaTeX

## Slide 2
FERMAT'S PRINCIPLE
Fermat's Principle: Statement and Physical Meaning
Pierre de Fermat (1662) stated that light travels between two points along the path for which the Optical Path Length is stationary — not necessarily minimum, but a saddle point of the OPL functional.
What 'stationary' means
OPL = ∫n ds measures the number of wavelengths along the path
Stationary: δ(OPL) = 0 means small path variations produce no first-order change in OPL
Usually a minimum (ordinary reflection/refraction)
Can be a maximum (e.g. rays through an ellipsoidal mirror at the far focus)
Can be a saddle point (some GRIN and resonator configurations)
Equivalent to the action principle in mechanics (Maupertuis)
Optical Path Length vs. time
OPL = n·(geometric length). Time of travel = OPL/c
In vacuum n=1: OPL = geometric length
In glass n=1.5: OPL = 1.5 × geometric length (phase accumulates faster)
Phase accumulated: φ = (2π/λ₀) × OPL = k₀ × OPL
Fermat's 'least time' (original 1662 statement) is a special case when n is constant in each medium

## Slide 3
FERMAT'S PRINCIPLE · SNELL
Deriving Snell's Law from Fermat's Principle
A ray crosses a flat interface between media n₁ and n₂. We minimise the total OPL over all possible crossing points x, with the geometry fixed (source height a, observation depth b, lateral separation d).
Snell derivation geometry
Interface
n₁
n₂
a
b
x
d-x
θ₁
θ₂
← d →
Step-by-step derivation
OPL(x) = n₁·(x/cosθ₁) + n₂·((d−x)/cosθ₂) [path lengths in each medium]
In terms of geometry: OPL = n₁√(a²+x²) + n₂√(b²+(d−x)²)
Stationarity: d(OPL)/dx = 0
d/dx[n₁√(a²+x²)] = n₁x/√(a²+x²) = n₁sinθ₁
d/dx[n₂√(b²+(d−x)²)] = −n₂(d−x)/√(b²+(d−x)²) = −n₂sinθ₂
Setting sum to zero: n₁sinθ₁ − n₂sinθ₂ = 0
⟹ n₁sinθ₁ = n₂sinθ₂ ✓ (Snell's law derived!)

## Slide 4
FERMAT'S PRINCIPLE · REFLECTION
Deriving the Law of Reflection from Fermat's Principle
A ray from source A at height a reflects off a flat mirror and reaches observer B at height b, with both on the same side of the mirror. We minimise OPL = total geometric path length (n=const).
Reflection geometry
Mirror (n₁ uniform above)
A
B
x
θᵢ
θᵣ
A'
Derivation & the mirror-image trick
OPL(x) = √(a²+x²) + √(b²+(d−x)²) [n=1 above mirror]
d(OPL)/dx = 0: sinθᵢ = sinθᵣ ⟹ θᵢ = θᵣ ✓
Equivalent construction: reflect source A to virtual image A' below mirror
Straight line A'→B is the shortest path: always gives θᵢ = θᵣ
The virtual-image construction is a direct consequence of Fermat
Applies to curved mirrors too: normal to mirror surface bisects i and r

## Slide 5
FERMAT'S PRINCIPLE · TIR
Total Internal Reflection & OPL Phase Accumulation
TIR from Fermat
At the critical angle θc = arcsin(n₂/n₁), the refracted ray grazes the interface at θ₂=90°
For θ₁ > θc, Snell's law gives sinθ₂ = (n₁/n₂)sinθ₁ > 1 — no real solution
From the OPL perspective: no stationary-OPL path exists through the interface
Energy cannot propagate as a real transmitted ray → total reflection
Evanescent wave: exponentially decaying field penetrates a few λ into medium 2
Evanescent coupling: tunnelling between closely spaced fibres/prisms (FTIR)
OPL and phase: practical consequences
Optical path difference (OPD) between two rays → phase difference Δφ = k₀·OPD
Δφ = 2πm → constructive (bright fringe in interferometer)
Δφ = (2m+1)π → destructive (dark fringe)
Anti-reflection coating: layer thickness t = λ/(4n) → OPL = λ/2 → Δφ = π → destructive reflection
AR coating condition: n_coat = √(n₁ n₂), t = λ₀/(4n_coat)
Fabry-Pérot: resonance when round-trip OPL = mλ (Lec 04, Lasers)

## Slide 6
FERMAT'S PRINCIPLE · LENSES
Lens Design: The Equal OPL Condition
A perfect imaging lens maps every ray from a source point to the same image point. By Fermat's principle this requires that all rays have the same OPL — the lens surface is precisely shaped to enforce this.
Equal-OPL lens construction
S
P
OPL₁ = OPL₂ = OPL₃ = const
Consequences of the equal-OPL condition
All rays from S to P have the same OPL → arrive in phase → constructive interference → bright image
A ray through the centre of the lens travels all in air → has smallest geometric length
A marginal ray (through edge) travels mostly in glass → geometric length larger but in glass (higher n) fewer wavelengths fit → OPL equalised
Aberrations arise when the lens surface deviates from the ideal equal-OPL shape
Aspherical lenses and multi-element designs aim to satisfy the OPL condition over a wider field

## Slide 7
FERMAT'S PRINCIPLE · VARIATIONAL
Variational Calculus: Euler–Lagrange and the Ray Equation
Fermat's principle is a variational principle — it says δ(OPL)=0 for the true ray. Applying the Euler–Lagrange equations to the OPL integral yields the general ray equation, valid in any medium.
Euler–Lagrange derivation outline
OPL = ∫n(r) ds with ds = √(dx²+dy²+dz²)
Treat y(x), z(x) as the unknown functions → Lagrangian L = n√(1+y'²+z'²)
E–L equation for y: d/dx(∂L/∂y') − ∂L/∂y = 0
In vector form: d/ds(n dr/ds) = ∇n (general 3D ray equation)
In uniform medium (∇n=0): d²r/ds²=0 → straight lines ✓
Analogy with mechanics: n plays the role of mass×speed (momentum)
Mechanics analogy
Fermat ↔ Hamilton's principle: δ∫L dt = 0
OPL ↔ action S = ∫p dq
n(r) ↔ refractive index momentum |p| = n
Ray equation ↔ Newton's law F = dp/ds
Snell's law ↔ conservation of tangential momentum
Hamiltonian optics (Lie group methods) uses this fully

## Slide 8
FERMAT'S PRINCIPLE · GRIN
Fermat in GRIN Media: Curved Ray Paths
In a gradient-index (GRIN) medium, ∇n ≠ 0, so the ray equation d/ds(n dr/ds) = ∇n predicts curved ray paths. The OPL of each curved ray is stationary — not minimum nor maximum in general.
Sinusoidal ray paths in GRIN rod
Quarter-pitch → collimate
Half-pitch → image
GRIN applications
Optical fibre: parabolic n(r) → all modes travel same OPL → minimal pulse spreading (GI fibre)
Selfoc® GRIN lenses: quarter-pitch collimates, half-pitch images — used in laser coupling, endoscopes
Human eye lens: graded n from cortex to centre reduces aberration
Atmosphere: temperature gradient bends light → mirages, astronomical refraction

## Slide 9
FERMAT'S PRINCIPLE · HUYGENS
Fermat's Principle and Huygens' Construction
Fermat's principle and Huygens' wavelet construction are two faces of the same physics. The OPL perspective gives rays; the wavefront perspective gives Huygens wavelets. Together they explain all of geometric and wave optics.
Wavefronts from OPL
Wavefront W(t): surface where OPL from source = constant
Rays are the orthogonal trajectories to wavefronts (normals)
In homogeneous medium: plane wavefronts → straight rays
At a curved surface: wavefront refraction described by Snell = OPL stationarity
Huygens: each point on W emits a spherical wavelet; next wavefront = envelope
The Lagrange–Helmholtz invariant
From Fermat: n sinθ is preserved at each ray-trace step along optical axis
Paraxial form: n y θ = const (Lagrange invariant)
Relates input and output beam properties for any optical system
A large-field, large-NA system cannot simultaneously have high magnification
Fundamental limit on throughput (étendue = n²A·Ω) in optical instruments
Summary: Fermat's principle (δOPL=0) → Snell's law + reflection law + GRIN ray equation + lens design condition + Lagrange invariant + wavefront construction — all from one variational statement.

## Slide 10
FERMAT'S PRINCIPLE · SUMMARY
Summary: Everything Derived from Fermat's Principle
δ OPL = 0
Fermat's Principle
Snell's Law
n₁sinθ₁=n₂sinθ₂
Reflection Law
θᵢ = θᵣ
TIR Condition
θc=arcsin(n₂/n₁)
GRIN Ray Equation
d/ds(n dr/ds)=∇n
Lagrange Invariant
n y θ = const
Lens Design
OPL = const for all rays
Wavefront / Huygens
rays ⊥ surfaces of const OPL
Phase Accumulation
φ = k₀ · OPL

## Slide 11
FERMAT'S PRINCIPLE · REFERENCES
Fermat's Principle: References, Problems & Projects
BSc References & Reading
Hecht, Optics, 5th ed. — Ch. 4.3–4.5: Fermat's principle, derivation of Snell's law, reflection.
Born & Wolf, Principles of Optics — Ch. 3.1–3.3: Fermat's principle and the eikonal equation.
Jenkins & White, Fundamentals of Optics — Ch. 1–2: Fermat and geometric optics.
Feynman, QED: The Strange Theory of Light and Matter — intuitive path-integral view of Fermat.
Feynman Lectures Vol. I, Ch. 26: 'Optics: the Principle of Least Time'.
MSc / Advanced References
Saleh & Teich, Fundamentals of Photonics — Ch. 1.3: ray optics from Fermat's principle.
Goodman, Introduction to Fourier Optics — App. A: OPL and phase in diffraction integrals.
Luneburg, Mathematical Theory of Optics (1964): rigorous variational optics, Hamiltonian formulation.
Arnold, Mathematical Methods of Classical Mechanics — Ch. 9: geometric optics as classical mechanics.
Sharma, Introduction to Computational Optics (2006): numerical ray-tracing from Fermat.
Problem Sets & Projects
[BSc] Starting from OPL(x)=n₁√(a²+x²)+n₂√(b²+(d−x)²), take d(OPL)/dx=0 and show it gives Snell's law exactly.
[BSc] Use Fermat's principle to show that a flat mirror satisfies θᵢ=θᵣ using the virtual-image construction.
[BSc] Prove that a plano-convex lens with R₁=∞ and n=1.5 satisfies the equal-OPL condition for a source at infinity when the curved surface has radius R = f(n−1).
[BSc] Show that the AR coating condition t=λ₀/(4n_coat) with n_coat=√(n₁n₂) follows from requiring OPD=λ/2 for the two surface reflections.
[MSc] Apply the Euler–Lagrange equations to OPL=∫n(r)ds to derive the ray equation d/ds(n dr/ds)=∇n in 3D.
[MSc] For a parabolic GRIN medium n(r)=n₀(1−αr²/2), solve the ray equation to show r(z)=r₀cos(√α z). Confirm with the ABCD matrix.
[MSc Project] Implement a numerical ray-tracer using Fermat's principle (OPL minimisation with Newton's method) and trace a paraxial ray through a biconvex lens. Compare with the thin-lens ABCD result.