## Slide 1
LECTURE 03c
Lasers & Coherent Light Sources
Population Inversion · Stimulated Emission · Resonators · Coherence · Laser Types
Linear Optics Course · All formulas typeset with LaTeX

## Slide 2
LASERS
Einstein Coefficients: Absorption, Spontaneous & Stimulated Emission
Einstein (1917) showed that an electromagnetic field interacting with a two-level atom produces three processes. The ratio of their rates is fixed by thermodynamics — and stimulated emission is the key to laser amplification.
Absorption
Rate: W_abs = B₁₂ ρ(ν) N₁
Atom in ground state |1⟩ absorbs photon hν → excited state |2⟩.
Rate proportional to radiation density ρ(ν) and population N₁.
Spontaneous Emission
Rate: W_sp = A₂₁ N₂
Excited atom decays randomly to |1⟩, emitting photon in random direction and phase.
Lifetime τ = 1/A₂₁. This is noise in a laser.
Stimulated Emission
Rate: W_st = B₂₁ ρ(ν) N₂
Incoming photon triggers |2⟩ → |1⟩ + identical photon.
Same frequency, phase, polarization, direction — coherent amplification!
Einstein relations and the condition for gain
B₁₂ = B₂₁ (absorption and stimulated emission coefficients are equal — symmetry)
A₂₁ = 8πhν³/c³ · B₂₁ (spontaneous emission increases steeply with frequency)
Net gain requires N₂ > N₁ (population inversion) — impossible in thermal equilibrium (Boltzmann: N₂/N₁=exp(−hν/kT) < 1)
Population inversion requires a pumping mechanism — 3-level or 4-level system

## Slide 3
LASERS
Population Inversion: 3-Level and 4-Level Systems
Thermal equilibrium always has more atoms in lower levels (Boltzmann). Pumping drives the system away from equilibrium. The key requirement: upper laser level lifetime τ₂ ≫ lower level lifetime τ₁.
3-level system (e.g. Ruby, 694nm)
3: pump band
2: upper laser level
(long lifetime τ~3ms)
1: ground state
pump
laser
694nm
Lower level = ground state → needs >50% inversion → hard to achieve
Requires strong pumping (flashlamp)
First laser (Maiman 1960): pulsed ruby
4-level system (e.g. Nd:YAG, 1064nm)
4: pump band
3: upper laser level (τ~230μs)
2: lower laser level (fast decay)
1: ground state
pump
laser
1064nm
Lower level depleted rapidly → easy inversion even at low pump
CW operation straightforward
Most practical solid-state and gas lasers

## Slide 4
LASERS
The Optical Resonator: Modes and Threshold
Two mirrors form a Fabry-Pérot resonator. The gain medium inside provides amplification; the mirrors provide feedback. Lasing starts when the round-trip gain equals the round-trip loss.
Fabry-Pérot laser cavity
HR
R=100%
OC
R<100%
Gain medium (stimulated emission)
Output
beam
L
Longitudinal modes & threshold
Resonance: round-trip phase = 2πm → ν_m = mc/(2nL)
Mode spacing: Δν = c/(2nL) (FSR — free spectral range)
Threshold: round-trip gain G = R₁R₂exp(2gL) ≥ 1
Above threshold: gain clamps to threshold; power grows in cavity
Transverse modes (TEM)
TEM₀₀ (fundamental Gaussian): lowest loss, best beam quality, M²=1
TEM₁₀, TEM₀₁ (Hermite-Gaussian): higher-order spatial modes
Ring/unstable cavities: different mode structure and output coupling
Mode selection: aperture inside cavity kills higher-order modes

## Slide 5
LASERS · COHERENCE
Laser Coherence: Temporal and Spatial
A laser's coherence properties follow directly from its spectral purity and the spatial quality of its mode. Both far exceed any thermal light source.
Temporal coherence
Coherence time: τc = 1/Δν (inverse of linewidth)
Coherence length: Lc = c·τc = c/Δν = λ²/Δλ
Single-mode HeNe (Δν~1MHz): Lc ≈ 300m
Multimode laser (Δν~1GHz): Lc ≈ 30cm
Thermal lamp (Δλ~1nm at 590nm): Lc ≈ 0.35mm
Interference fringes visible only for path difference < Lc
Holography requires Lc larger than depth of object
Spatial coherence
Spatial coherence: correlation of E-field across the beam wavefront
Single transverse mode (TEM₀₀): fully spatially coherent across beam
Spatial coherence radius: rc ≈ λ/(2θ_div) (van Cittert–Zernike)
Fully coherent beam: can be focused to a diffraction-limited spot
M² = 1: ideal Gaussian. Real beams M²>1
Sun: spatially coherent over only ~0.1mm (small angular diameter)
Required for laser cutting, holography, coherent LiDAR
Schawlow-Townes linewidth: Δν_min = 2πhν(Δν_cavity)²/P_out — quantum limit. Single-mode semiconductor lasers approach this.

## Slide 6
LASERS · TYPES
Laser Types: A Gallery of Coherent Sources
He-Ne (gas) — λ = 632.8 nm
DC discharge tube; 4-level; cw; M²≈1.05. Holography, metrology. Δν<1MHz possible.
Nd:YAG (solid state) — λ = 1064 nm
Flashlamp or diode-pumped; Q-switch → ns pulses; SHG→532nm. Material processing, ranging.
Ti:Sapphire (tunable) — λ = 700–1000 nm
Tunable ultrabroadband; mode-locked → <10 fs pulses; pumped by 532nm. Ultrafast science.
CO₂ (gas) — λ = 10.6 μm
IR; kW average power possible; cutting/welding steel. Gas flow cooling required.
Diode (semiconductor) — λ = 375–2000 nm
Electrically pumped p-n junction; tiny, efficient, cheap; M²~2–10. Telecom, pumping, LiDAR.
Fibre (Er:fibre) — λ = 1550 nm
Er³⁺ doped SiO₂ fibre; cw or pulsed; excellent beam quality; used in telecom amplifiers (EDFA).
Excimer (UV) — λ = 193–351 nm
KrF 248nm, ArF 193nm; pulsed; UV lithography (chip manufacture), eye surgery (LASIK).
Free-Electron Laser — λ = tunable, X-ray
Relativistic electrons wiggling in undulator → coherent X-rays. Brightest X-ray source; large facility.

## Slide 7
LASERS · REFERENCES
Lasers & Coherence: References, Problems & Projects
BSc References & Reading
Hecht, Optics, 5th ed. — Ch. 13: lasers. Clear undergraduate treatment.
Saleh & Teich, Fundamentals of Photonics — Ch. 14–15: laser amplifiers and oscillators.
Yariv & Yeh, Photonics (2006) — Ch. 5–6: laser oscillation, coherence.
Svelto, Principles of Lasers, 5th ed. (2010): comprehensive from Einstein coefficients to ultrafast.
MSc / Advanced References
Siegman, Lasers (1986) — University Science Books. The definitive graduate text.
Saleh & Teich, Fundamentals of Photonics — Ch. 11: Coherence theory (temporal and spatial).
Mandel & Wolf, Optical Coherence and Quantum Optics (1995): rigorous coherence theory.
Diels & Rudolph, Ultrashort Laser Pulse Phenomena (2006): mode-locking, fs pulses.
Schawlow & Townes (1958) Phys. Rev. 112, 1940: original laser proposal paper.
Problem Sets & Projects
[BSc] For a 1m long HeNe laser cavity (n≈1), find the FSR and the approximate number of cavity modes under the 1.5 GHz gain bandwidth.
[BSc] Show that for a 4-level system, the threshold inversion density is N_th = α_loss/(B₂₁ · hν · τ_rt). Explain each symbol.
[BSc] Calculate the coherence length of (a) a single-mode HeNe laser with Δν=1 MHz, (b) a multimode diode laser with Δλ=3nm at 780nm.
[MSc] Derive the Schawlow-Townes linewidth formula from the spontaneous-emission noise model. What limits real lasers above this?
[MSc Project] Model a Gaussian-beam resonator using ABCD matrices. Find the eigenmode waist for a plano-concave cavity (L=300mm, R=500mm) at 1064nm.